## Slide 1: Multi-Core Packet Scattering to Disentangle Performance Bottlenecks
Yotam Harchol
The Hebrew University
Joint work with Y. Afek, A. Bremler-Barr, D. Hay and Y. Koral.
This work was supported by European Research Council (ERC) Starting Grant
no. 259085, and appeared in HPSR'11 and ANCS’12.
Notes: affiliations

## Slide 2: Network Intrusion Detection Systems
Internet
Very popular middlebox
  May be deployed in various places within the network
Reports or drops malicious packets
  How to identify malicious packets?
Notes: Prevent attacks on applications in the network

## Slide 3: Deep Packet Inspection (DPI)
Search for malicious patterns within packets’ payload
  Exact string patterns/signatures
  Patterns defined as regular expressions
  Often combined with information from header fields
DPI is the heaviest processing component of NIDS
  Why not use many machines/cores to speed it up?
Pipeline multi-core, not efficient.
  Imbalance of pipeline stations, DPI much heavier
Parallel multi-core?

## Slide 4: Multi-Core Deep Packet Inspection (DPI)
Option 1: Each core scans for a subset of the pattern-set
Core 1
Core 2
Core 3
Core 4
Pattern Set 1
Pattern Set 2
Pattern Set 3
Pattern Set 4
Notes: This option is less efficient because scanning time per byte is usually constant (?)
Independently of the size of pattern set, except for the cases I will discuss later

## Slide 5: Multi-Core Deep Packet Inspection (DPI)
Option 2: All cores are the same,
Load-balance between cores
Core 1
Core 2
Core 3
Core 4
DPI
DPI
DPI
DPI
Notes: Load balance packets or flows between the cores

## Slide 6: Complexity DoS Attack Over NIDS
Regular operation
2 Steps attack:
Attacker
2. Launch original attack (e.g., steal credit cards)
1. Kill IPS/FW
normal
malicious
heavy
Internet
Malicious packets aim to hurt the application
  NIDS should be able to deal with them with no degradation in performance
Heavy packets aim to hurt the NIDS
  They will do nothing to the application
Notes: We present "heavy" packets
Exploit the gap between the average and worst case performance

## Slide 7: Attack on Security Elements
Combined Attack: DDoS on Security Element exposed the network – theft of customers’ information
Notes: May 2011

## Slide 8: Attack on Snort
The most widely deployed IDS/IPS worldwide.
Heavy packets rate
Notes: Real-life HTTP traces, alexa
Throughput: the total number of traffic handled by the NIDS
Goodput: the total number of traffic handled by the NIDS not including the heavy packets

## Slide 9: OUR GOAL:
MCA2: Multi-Core Architecture for Mitigating Complexity Attacks

## Slide 10: Airline Desk Example
Notes: ----- Meeting Notes (10/17/13 12:26) -----
Let's start with an example from a different domain

## Slide 11: Airline Desk Example
Boarding pass, please
Notes: התקפה
כל הארבע מקבלות חבילה גדולה

## Slide 12: Airline Desk Example
20 min.
An isle seat near window!!
Three carry on handbags!!!
Free first class upgrade!!
Can’t find passport!!
Overweight!!!
1 min.
Notes: התקפה
כל הארבע מקבלות חבילה גדולה

## Slide 13: Airline Desk Example
Notes: התקפה
כל הארבע מקבלות חבילה גדולה

## Slide 14: Airline Desk Example
4 min.
1 min.
Domain Properties
Heavy & Light customers.
Easy detection of heavy customers.
Moving customers between queues is cheap.
Heavy customers have special more efficient processing method.
Special training
packets
packets
packets
packets
Notes: התקפה
כל הארבע מקבלות חבילה גדולה

## Slide 15: Some packets are much “heavier” than others
The Snort-attack experiment
Property 1 in Snort Attack

## Slide 16: Snort uses Aho-Corasick DFA
DPI mechanism is a main bottleneck in Snort
Allows single step for each input symbol
Holds transition for each alphabet symbol
Fast & Huge
Best for normal traffic
Exposed to cache-miss attack
Cache
Main Memory

## Slide 17: Crafting HEAVY packets
Snort patterns database
Heavy packets factory
Chop last
2 bytes

## Slide 18: Snort-Attack Experiment
Cache
Main Memory
Normal Traffic
Attack Scenario
Cache-miss!!!
Does not require many packets!!!
Domain Properties
Heavy & Light packets.
Easy detection of heavy packets
Moving packets between queues is cheap.
Heavy packets have special more efficient processing method.
Notes: כל צעד זה cache miss

## Slide 19: Detecting heavy packets is feasible
Property 2 in Snort Attack

## Slide 20: How Do We Detect?
Common states are detected through training traffic set
threshold
non-common states percentage
Tradeoff: Attack effectiveness vs. false positive/negative rates
Notes: Two distribution functions

## Slide 21: How Do We Detect?
Common States
Non
Common States
Heavy packet :
# Not Common States
# Common States
≥
α
After at least
20 bytes

## Slide 22
Domain Properties
Heavy & Light packets.
Easy detection of heavy packets
Moving packets between queues is cheap.
Heavy packets have special more efficient processing method.

## Slide 23: System Architecture
Processor Chip
Core #8
NIC
Core #1
Q
Core #2
Q
Q
Q
Q
Detects heavy packets
Core #9
Core #10
Routine Mode:
Load balance between cores

## Slide 24: System Architecture
Processor Chip
Core #8
Dedicated Core #9
NIC
Core #1
Q
Core #2
Q
Q
Q
B
Dedicated Core #10
B
Q
Detects heavy packets
Alert Mode:
Dedicated cores for heavy packets
Others detect and move heavy to Dedicated.
B
B

## Slide 25: Inter-Thread Communication
Non-blocking IN-queues
  Single reader, single writer, lock-free queues
Dedicated cores in-queues are blocking (using test&set locks)
  Non-dedicated threads “steal” packets from the HoL when sending a heavy packet
Processor Chip
Core #8
Dedicated Core #9
NIC
Core #1
Q
Core #2
Q
Q
Q
B
Dedicated Core #10
B
Q
B
B

## Slide 26: Inter-Thread Communication
In queues and Heavy packets queues are lock-free – no locking mechanisms are used
Cyclic queue, conflicts are resolved by marking two phases on the queue.
  Changes after the entire queue is written to
Writer writes to the queue from right to left:
  Check whether reader_phase=writer_phase or tail>head; otherwise queue is full
  Right_phase  writer_phase
  Write packet_pointer + offset
  Left_phase  writer_phase
Reader reads in the opposite direction:
  First reads left_phase bit, then packet, then right_phase bit.
  If left_phase != right_phase: record is being written; retry.
  If left_phase = right_phase != reader_phase: queue is empty
  Otherwise, valid packet is read

## Slide 27
Domain Properties
Heavy & Light packets.
Easy detection of heavy packets
Moving packets between queues is cheap.
Heavy packets have special more efficient processing method.

## Slide 28: Snort uses Aho-Corasick DFA
Huge memory footprint
Single memory access per input symbol
Small memory footprint
Multiple memory accesses per input symbol
Notes: COMPRESSION TRADES SPACE FOR TIME

## Slide 29: Full Matrix vs. Compressed
Heavy packets rate
In cache
Not in cache
Always in cache
Multiple
memory accesses
per symbol
One memory access per symbol
Notes: END: If we have a core that mostly handles heavy packets, it might be good to use the compressed implementation

## Slide 30
Domain Properties
Heavy & Light packets.
Easy detection of heavy packets
Moving packets between queues is cheap.
Heavy packets have special more efficient processing method.

## Slide 31: Experimental Results
Notes: We implemented the system and…

## Slide 32: System Throughput Over Time
Reaction time can be smaller
Notes: We implemented the system and…

## Slide 33: Different Algorithms Goodput
Bandwidth
Attack
Complexity
Attack
Notes: Goodput is the throughput on "good" packets
The higher the attack bandwidth is, less "good" packets exist

## Slide 34: Additional Application for MCA2
The Hybrid-FA-attack experiment
Notes: The approach is general, as long as the properties are satisfied
Here is another experiment we made that shows that

## Slide 35: Hybrid-FA
Space-efficient data structure for regular expression matching
Faster than NFA
Structure:
  Head DFA
  Border states
  Tail DFAs
More than one state can be active at the same time!
s0
s7
s12
s1
s2
s3
s5
s4
C
C
E
D
B
E
D
s14
s13
s6
D
s8
B
s9
C
s10
A
s11
B
A
A
.*
[^\n]*

## Slide 36: Hybrid-FA Attack
Normal Traffic
Attack Scenario
Again: Does not require many packets!!!
s0
s7
s12
s1
s2
s3
s5
s4
C
C
E
D
B
E
D
s14
s13
s6
D
s8
B
s9
C
s10
A
s11
B
A
A
.*
[^\n]*
s0
s7
s8
s9
s10
s11
s12
s2
s5
s13
Input:
C
D
B
B
C
A
B

## Slide 37: Heavy Packet Detection
threshold

## Slide 38: MCA2 With Hybrid-FA

## Slide 39: Concluding Remarks
A multi-core system architecture, which is robust against complexity DoS attacks
This talk focused on specific NIDS and complexity attack
  But also shows other NIDS (e.g., Hybrid-FA)
  More issues are dealt in the paper (e.g., dealing with flows rather than single packets etc.)
We believe this approach can be generalized (outside the scope of NIDS).

## Slide 40: Thank You!!

## Slide 41: Extra Slides…

## Slide 42: Detection Tradeoff
Attacker can use "lighter" heavy packets to get below threshold
Chart: Attack Intensity
| 0.0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1.0
Very Light | 0.00023333 | 0.00018 | 0.00016333 | 0.00015333 | 0.00013333 | 9.6667e-05 | 0.0001 | 6e-05 | 4e-05 | 3.6667e-05 | 0
Light | 0.00026 | 0.00019333 | 0.00019 | 0.00014667 | 0.00014667 | 0.00014 | 8.6667e-05 | 5e-05 | 6.6667e-05 | 2e-05 | 0
Medium | 0.000206 | 0.000176 | 0.000196 | 0.000162 | 0.000128 | 0.000128 | 8.8e-05 | 5.8e-05 | 3.8e-05 | 2.4e-05 | 0
Semi-Heavy | 1e-05 | 6e-06 | 6e-06 | 0 | 2e-06 | 0 | 4e-06 | 4e-06 | 2e-06 | 0 | 0
Heavy | 4e-06 | 8e-06 | 4e-06 | 2e-06 | 0 | 2e-06 | 2e-06 | 0 | 2e-06 | 0 | 0
Very Heavy | 2e-06 | 4e-06 | 4e-06 | 2e-06 | 6e-06 | 0 | 4e-06 | 0 | 0 | 0 | 0
Chart: Attack Instensity
| 0.0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1.0
Very Light | 0 | 0.027263 | 0.05401 | 0.082083 | 0.10793 | 0.13581 | 0.16327 | 0.18957 | 0.21794 | 0.24342 | 0.27028
Light | 0 | 0.01701 | 0.03522 | 0.05161 | 0.06959 | 0.086167 | 0.103 | 0.11956 | 0.1374 | 0.15549 | 0.17166
Medium | 0 | 2e-05 | 2.8e-05 | 4.6e-05 | 5.2e-05 | 8.4e-05 | 9e-05 | 0.000114 | 0.000106 | 0.000144 | 0.000138
Semi-Heavy | 0 | 2e-06 | 0 | 2e-06 | 2e-06 | 0 | 0 | 2e-06 | 0 | 4e-06 | 4e-06
Heavy | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Very Heavy | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
non-common states percentage
Percentage of packets
"Regular" traffic
Different attack traffic
With growing "heaviness"
Medium
Semi-Heavy
Heavy
Very Heavy

## Slide 43: Detection Tradeoff
The effect of "lighter" packets on throughput
Chart: Attack Intensity
| 0.0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1.0
Very Light | 9261.1358 | 8355.8887 | 8450.9116 | 7985.3672 | 7695.655 | 7238.9068 | 7147.2201 | 6808.9436 | 6886.8541 | 6371.4823 | 6253.4045
Light | 9279.7804 | 8272.9139 | 7844.4506 | 7329.3939 | 6834.046 | 6381.646 | 6369.0003 | 5976.2254 | 5773.4196 | 5397.5796 | 5371.0935
Medium | 8923.9338 | 7568.1252 | 7235.9699 | 7125.65 | 5436.5154 | 5309.5718 | 4496.1783 | 4191.9394 | 3851.6166 | 3691.9664 | 3454.6904
Semi-Heavy | 8338.5343 | 7445.101 | 6906.0192 | 6729.5384 | 5547.6589 | 5448.8813 | 3694.1631 | 3983.0348 | 3145.4118 | 3155.1975 | 3161.8634
Heavy | 9019.635 | 7257.5917 | 7050.7704 | 5755.5001 | 5165.0575 | 4789.3956 | 4244.3728 | 4142.4022 | 3177.2905 | 3202.1669 | 3199.1013
Very Heavy | 8954.1656 | 7021.3 | 6946.7127 | 5864.4534 | 5290.3379 | 4828.5779 | 3705.1904 | 4315.0234 | 3364.9581 | 3422.9404 | 3496.1377
-23%
-62%
-66%
-17%
-41%
-44%